Using the FEM Laplacian in Deepsphere

---
Goal
- Ability to use Convolutional Neural Networks on spherical data (weather/space maps...)
- Have it be rotation-equivariant by design
- Have it be efficient !

---
What has been done
- Deepsphere uses a graph to approximate the sphere,
- It uses a convolutional NN,
- It uses the Graph Laplacian to approximate the sphere’s Laplace-Beltrami operator.
Explanation next slide !

---
Without approximations
- The sphere is a manifold, with a defined “Laplace-Beltrami operator” : Δ.
- We want to do convolutions.
  These are easy in Fourier space.
- Fourier transform = a decomposition relative to Δ’s eigenfunctions.

---
Graph approximation
- Let’s approximate the sphere with a graph,
- Sample nodes on the sphere with HEALPix,
- Define weighted edges somehow* → Graph!
- We can define a Laplace Operator for it!
* For the HKGL :
w_{ij} = \exp(-\frac{||v_i-v_j||^2}{4t})

---
Graph approximation
- The (discrete) Graph Laplacian L :
- Matrix representation of Δ,
- Graph sparsely connected ⇒ L sparse,
- Graph undirected ⇒ L symmetric.
\textbf{L} = \textbf{D} - \textbf{W}

---
Graph convolutions
- L is eigendecomposable :
- Define Fourier Transform :
- Define “a filter” :
- Define convolution :
(Finally, use polynomial filters for efficiency)
\mathbf{\hat x} = \mathbf{U}^\mathrm{T}\mathbf{x}
\textbf{L} = \mathbf{U\Lambda U}^\mathrm{T}
\mathbf{y} = \mathcal{F}_G^{-1}(\mathbf{K\hat{f}}) = \mathbf{UK\hat{f}} = \mathbf{UKU}^\mathrm{T}\mathbf{f} = \mathbf{U}h(\mathbf{\Lambda})\mathbf{U}^\mathrm{T}\mathbf{f}
h : \lambda \mapsto h(\lambda)

---
Graph Laplacian’s problems
- How to get convergence of L’s eigenvectors to the real Δ’s eigenfunctions?
- HKGL converges if the graph...
  - fully connected (⇒not sparse)
  - nodes equi-area-sampled* (⇒not easy) & filter width t well-tuned.
* It still ~works if the sampling is regular enough

---
FEM approximation
- Approximate sphere with a triangulation T
- Discretize signals on that
- Turns out that FEM filtering ≅ Graph filtering
- FEM Laplacian still converges with more irregular samplings !

---
FEM explanation (see board)
- We want Δ’s eigenfunctions, find f :
- Insert test function ν + integrate by parts :
  (find f such that this holds for all ν in our function space)
\Delta f = -\lambda f
\int_{\mathbb{S}_2} \nabla f(x) \cdot \nabla v(x)\mathrm{d}x = \lambda \int_{\mathbb{S}_2} f(x) \cdot v(x)\mathrm{d}x

---
FEM explanation (see board)
- ν ∈ continuous piecewise-linear funcs on T
- T has a basis :
- Just prove for all bases :
  with
\phi_i(x_j) = \delta_{ij} ~~ \forall x_j \in \mathcal{T} ~~ \forall i \in [0, n-1]
\left\{\begin{array}{lll} (\textbf{A})_{ij}&=&\int_{\mathbb{S}_2}\nabla\phi_{i}(\textbf{x})\cdot\nabla\phi_{j}(\textbf{x})\mathrm{d}\textbf{x}\\ (\textbf{B})_{ij}&=&\int_{\mathbb{S}_2}\phi_{i}(\textbf{x})\phi_{j}(\textbf{x})\mathrm{d}\textbf{x}\\ (\textbf{f})_{i}&=& f_i : f(\textbf{x}) = \sum_{k=0}^{n-1} f_k\phi_k(\textbf{x}) \end{array}\right.
\textbf{Af} = \lambda\textbf{Bf}

---
FEM explanation (see board)
- Define FEM Laplacian :
- A and B as full as triangles share vertices
- A and B symmetric
- L not sparse, nor symmetric!
  ⇒ We will use tricks
\textbf{L} = \textbf{B}^{-1}\textbf{A}

---
HKGL	FEM L
HEALPix
Equiangular
HKGL vs FEM L

---
Neural network
- Computes any function, given enough nodes
- Can be “trained” by descending gradients
- This one is fully connected ⇒ heavyweight

---
Convolutional neural network
- Translation-equivariant feature extraction
- Less connected + shared parameters ⇒
  lightweight

---
Deepsphere’s conv layers
- Use polynomial filters :
- Simpler convolution :
- Compute powers of L iteratively :
- Convolution : a full, but small K K matmul
h(\lambda) = \sum_{k=0}^{K-1} \theta_k \lambda^k
\mathbf{y} = \sum_{k=0}^{K-1} \theta_k \mathbf{L}^k\mathbf{f}
\left\{\begin{array}{lll} \mathbf{L}^0\mathbf{f}& =& \mathbf{f} \\ \mathbf{L}^{k+1}\mathbf{f}& =& \mathbf{L} ~ \cdot ~ \mathbf{L}^k\mathbf{f} \end{array}\right.
\times

---
Our FEM modifications
- B can be Cholesky-decomposed :
- C triangular + sparse like B ⇒ faster solving!
\mathbf{B} = \mathbf{CC}^\mathrm{T}

---
Our FEM modifications
- The FEM Laplacian isn’t sparse nor symmetric
- Powers of L must be computed another way :
- Solving can be optimized because B sparse!
- But B is symmetric and positive-definite too!
\left\{\begin{array}{lllll} \mathbf{L}^0\mathbf{f}& =& \mathbf{f} \\ \mathbf{L}^{k+1}\mathbf{f}& =& \mathbf{L} ~ \cdot ~ \mathbf{L}^{k}\mathbf{f}& \Rightarrow & \mathbf{B}\cdot(\mathbf{L}^{k+1}\mathbf{f}) = (\mathbf{A}\mathbf{L}^{k}\mathbf{f}) \end{array}\right.

---
Our FEM modifications
- Sadly, tf has no “sparse_cholesky_solve“
- This forces C to be full in every conv layer…
  ⇒ tf limits us to 2GB/tensor ⇒ nside≤32
- That was for powers of L. Convolution is still just a K K matmul.
\times

---
Recapitulation
- Defined a more robust FEM Laplacian
- Computed A, B, C for it
- Added them in Deepsphere’s models
- Made it work, except for some loss problems
- Learned more about differential geometry, discrete signal processing, FEM, deep learning.